## Slide 1: Load security on different Super-structures
The European project ICT-DRV online training course “Load Security”

## Slide 2: Requirements on superstructures
What is transported?
How is the good packed?
What quantity is transported?
What external conditions need to be considered?
What transport routes are planned?

## Slide 3: Superstructures
Curtainsider/ Curtainsider „Code XL“
Box (with or without side doors)
Open flat
Cover/ Stake

## Slide 4: Weight carrying capacity

## Slide 5: Box

## Slide 6: Cover/ stake

## Slide 7: Curtainsider

## Slide 8: Curtensider „Code XL“
nach DIN EN 12642

## Slide 9: Load distribution
Source: LVP v4.0

## Slide 10: Centre of gravity (sres)
Sres = -------------------
m1 x S1 + m2 x S2 + m3 x S3
m1 + m2 + m3
m = Weight of the good (t)
S = Centre of gravity to front wall (m)

## Slide 11
m1 + m2 + m3
m1 x S1 + m2 x S2 + m3 x S3
5,1 m
S3 = 5,1 m
3.000 kg
3.000 kg
m3 = 3.000 kg
2,4 m
S2 = 2,4 m
5.000 kg
5.000 kg
m2 = 5.000 kg
0,6 m
S1 = 0,6 m
2.000 kg
2.000 kg
m1 = 2.000 kg
Sample calculation „Centre of gravity of different pieces of cargo“
m1
m2
m3
s1
s2
s3
1,2m
2,4m
3,0m
Sres =
1.200 kg/m
12.000 kg/m
15.300 kg/m
10.000 kg
28.500 kg/m
2,85 m

## Slide 12: Lashing points

## Slide 13: Number of lashing points

## Slide 14: Labelling of lashing points
Lashing point label based on DIN EN 12640
Lashing point label incl. Handling instructions
Lashing point label incl. Handling instructions

## Slide 15: Weight carrying capacity of lashing points
800 daN
1.000 daN
1.000 daN
2.000 daN
3,5 – 7,5 t
7,5 - 12 t
More than 12 t
Lashing point front wall

## Slide 16
www.project-ICTDRV.eu Preparing and updating professional drivers‘ skills and competences with multimedia-based learning.